## Tehničke karakteristike IC-F5022 / IC-F6022
## General
			IC-F5022	IC-F6022
Frequency coverage			136–174MHz	400–470MHz
Number of channels			Max. 128 Ch/ 8 zones
Channel spacing			2.5/20/25kHz
Type of emission			16K0F3E, 14K0F3E, 8K50F3E
Current drain (approx.)	Tx	25W	5.0A
	Rx	Max. audio	0.7A
		Stand-by	250mA
Dimensions (projections not included; W×H×D)			150×40×117.5 mm
Weight			0.8kg (approx.)

## Transmitter
	IC-F5022	IC-F6022
RF output power	25W
Spurious emissions	0.25μW (≤ 1GHz) 1.0μW (> 1GHz)
Frequency stability	±1.5kHz
Audio harmonic distortion	3% typical 40% deviation
FM Hum and Noise	-

## Receiver
	IC-F5022	IC-F6022
Sensitivity at 20dB SINAD	–4dBμV (typ.)
Adjacent channel selectivity (WM/N)	75dB/75dB/65dB (typ.)
Spurious response rejection	80dB (typ.)
Intermodulation rejection	67dB (typ.)
AF output power (at 5% distortion with an 4 Ω load)	4W (typ.)